## Slide 1: Journal of Geophysics & Remote Sensing
New technologies of TEM in China
Guoqiang Xue, Weiying Chen, Dongyang Hou
Institute of Geology and Geophysics, Chinese Academy of Sciences

## Slide 2: OUTLINES
1. Introduction
2. new technology1-Infinitesimal point charge
3. new technology2-Electric source short-offset TEM
4. new technology3-Modified central loop TEM
5. new technology4-EM pseudo-seismic imaging
6. Reference

## Slide 3: 1. Introduction
Transient electromagnetic method（TEM）is a time domain method in electromagnetic exploration, which is sensitive to conductive targets and have been widely used in mineral source, coal, ground water, environment and engineering investigation(Nabighian,1991).
1.1 TEM Introduction

## Slide 4: 1. Introduction continued
1.2 Some vital issues in TEM exploration
Understand and calculate the TEM response base on its physical mechanism.
Greater investigation depth is needed to meet the need from deep mineral deposits and coal hydrogeology.
Higher precision and faster detection for both shallow and deep investigation.
Efficient processing method suitable to 2D and
3D data.

## Slide 5: 2. Infinitesimal Point Charge
2.1 Traditional approach to calculate TEM response
due to a finite source
1). Regard the source as a dipole(Kaufman,1987) 2). Regard the source as a superposition of many
dipoles(Nabighian,1991)
The relative error drops with the decrease of dipole dimension. The smallest and intrinsic source should be point charge

## Slide 6: 2. Infinitesimal Point Charge continued
t

 xx 2

 1 J x, 
  x,  
Te
4t   dxd


 



0 D  

 
2.2 Basis
According to Maxwell equations so long as an electric charge varies with time it will
excite electromagnetic wave .
2.3 Mathematics
Based on point charge hypothesis, TEM field analytical solution has been derived by introducing time-domain Green function. Integral formula has been used to transform electromagnetic field damping wave equation into Green function integral form. Auxiliary path has been constructed for solving singularity problem. Four heavy generalized integral formula of time-domain electromagnetic field response has been arrived by using Jordan's lemma, the residue theorem and generalized function method. Direct-time-domain exact solution of D’Alembert equations firstly has been derived(Zhou,2013;Xue,2014).
E(x, t) 

## Slide 7: 2. Infinitesimal Point Charge continued
2.4 Comparison with dipole
Solid line represents infinitesimal point charge (left figure) and measured data
( right figure), dashed represents dipole (both figures)
It is shown that the field of the infinitesimal point charge in the near source zone is different from that of dipole, whereas the far-source zone fields of these two sources are identical. The comparison of real and simulated data shows that the infinitesimal point charge represents the real source better than dipole source.

## Slide 8: 3. Electric Source Short-offset TEM
3.1 Background
Loop source excites only horizontal induction current, while grounded wire source has both horizontal and vertical induction current. This leads to loop source TEM only sensitive to conductive targets.
  Detection depth of loop source TEM usually is shallower than 1km.
  Difficult to lay the transmitting loop at mountain areas.

## Slide 9: 3. Electric Source Short-offset TEM continued
3.1 Background Continued
LOTEM(Strack,1992)
Advantage: great detection
depth (more than10km)
Disadvantages: great source- receiver distance (2~20Km), weak signal, volume effect, poor precision,
MTEM(Ziolkowski,2007)
Advantage: great power, pseudorandom transmitting source; multi-channel array, multi component, 3D detection; Pseudo- seismic imaging of data
Disadvantage: heavy, hard to conduct at mountain area; mainly used in marine; systemic and robust equipment have not been introduce to china

## Slide 10: 3. Electric Source Short-offset TEM continued
3.2 Definition
Short-offset TEM (abbreviated to SOTEM) means that the distance between transmitter and receiver is approximately equal to or less than the exploration depth(Xue,2013).
Typical SOTEM layout diagram

## Slide 11: 3. Electric Source Short-offset TEM continued
3.3 Observation area for each EM component
5
3
90o
x
y
3
5
90o
60o 60o
y
4
4 4
70o 70o
70o 70o
4
x
x
y
5 160o
160o 5
4
4
4
x
4
70o 70o
70o
70o
x
5
5
3
90
o
60o
90o
3 60o
x
y
3
3
160
o
Eyx
160o
Eyy
Ez
Hx
Hy
Hz

## Slide 12: 3. Electric Source Short-offset TEM continued
3.4 All-time apparent resistivity
1E-005
0.0001
0.001
0.01
0.1
1
1E-005
0.0001
0.001
0.01
0.1
1
10
100
1000
10000
100000
type H
all time
early time late time
  
t(s)
r 1=100W.m h1=500m
r 2=10W.m h2=500m
r 3=100W.m
0.0001
0.001
0.01
0.1
1
10
100
1000
p2
50
25
10
5
Calculated by polynomial fitting method
Calculated by dichotomy method

## Slide 13: 3. Electric Source Short-offset TEM continued
3.5 Imaging
Electric field underneath the Tx
2
x
u
E (z,t)= Ilρ [erf(
)- 1 +( 2u- 1 )(1+ u
2
)e-u /2 ]
πz3
2 π 2 2
2
Time of maximum of Ex for a given depth
z=zimage
dEx(z,t)
=0
dt
Image depth
image
z2 (t)
= 4t
μ0σ
Hz from a current filament located at image depth
z
H 
I y x  L x  L
4 y2  z2 ((x 1)2  y2  z2 )1/ 2 ((x 1)2  y2  z2 )1/ 2
slowness
0
dt = 1 zμ σ
dz 2
Conductivity of the image
0
2 d2 t

 dz2
Source image for a
three-layer model

## Slide 14: 3. Electric Source Short-offset TEM continued
3.6 Case study
Investigation of hydrous coal mine in Shandong Province
Discovery of Dawangzhuang Iron Ore in Anhui Province

## Slide 15: 4. Modified Central Loop TEM
Regular central loop
TEM has only one survey point at once layout, which leads to energy waste and low work efficiency
4.1 Reasons
The vertical magnetic
response in the central
part of loop is Approximately equal (Xue,2012)
The modified device
utilize the signal from a bigger central part which about 1/3 of loop area.

## Slide 16: 4. Modified Central Loop TEM continued
4.2 Modified theory
1
z
I0
k2a3
H () 
[3 (3  3k a  k2a2 )ek1a ]
1 1
3
2
a
t
5t Bz (t)
4t
 2I a2 
 L (t)  0 ( 0 0 )
2 2
0
0 1 2 1 3 1
2 3
1
z
I
k a
k1a
H () 
[Z (r) (Z (r)  Z (r)k a  Z (r)k a )e ]
0 1
0 0
2
3
L
z
a
60t
u Z (r) I 
 (
B (t)
)  [
 t
B(t) ]
t
t
Central loop
Modified Central loop

## Slide 17: 4. Modified Central Loop TEM continued
4.3 Modified instruments
Air coil:
heavy
and with small
receivearea(100m2)
Magnetic probe: portable and with great receive area
(10000m2, 20000m2)
Probe 1
coil
Probe 2
0.01
0.1
10
1
t/ ms
10000
1000
100
10
1
0.1
0.01
Significantly
increase the signal strength

## Slide 18: 5. TEM Pseudo-seismic Imaging

5.1 Basic theory(Xue,2013)
Background
1). The precision in TEM prospecting is relative low compare with seismic method 2). Interpretation and judgment always be made based on experience of interpreter 3). 2D and 3D TEM inversion are time-consuming and expensive.
For the aim to improve the precision, can we interpret TEM data similar to seismic
method?
Basic equation construction
Diffusion equations for TEM
2
 2
   U(r, )   (r)
U(r, )  0
0
1
2  t3
  2
Hm (t) 
  e 4tU ( )d
 
H(r, p2 )  U(r, p)
 Hm (r,t)   (r) t Hm (r,t)  0
Diffusion equations for seismic
Inverse Laplace transform
1
2
2
1
1
3
n
2
j
i
4ti
4ti
ti
n1
j 2
q
q
q
H 
2 1 1  j
( n  n1 )Um )
j 1  j 1 )U j  ne
(
(  )U  2  e
( e
2 t
Discrete

## Slide 19: 5. TEM Pseudo-seismic Imaging continued
5.2 Key techniques
Wavelet extraction
Kirchhoff integral function
1 


 

u(x, y, z,t)  

[u] (1)  1[ u ]  1 r [ u ]dQ  F
4 Q  n r r n vr n t  r0

----main idea of calculation
1). normalize method has been adopted,
2). optimizing normalizing parameter have
been selected by deviation theory 3).Newton iterative form to be used to make
the transformed wave field stable and
reliable.
Migration imaging

## Slide 20: 5. TEM Pseudo-seismic Imaging continued
5.3 Models simulation
1  5 m,
h1  80m
2  500  m
1  1  m,
h1  60m
2  10 m, h2  60m
3  100  m
1  10  m
2  300  m
h  70m

## Slide 21: 5. TEM Pseudo-seismic Imaging continued
5.4 Case study
Recognizing electrical interface
in Shanxi province
Detecting deep electric structure and distribution in Guangdong province

## Slide 22: 6. Reference
G.Q. Xue, Gelius, L.Xiu 3-D Pseudo-seismic Imaging of TEM data– a Feasibility Study. Geophysical
Prospecting, 2013, 61(S1), : 561–571doi:10.1111/j.1365-2478.2012 . 01109.
Guo-Qiang X, Wei-Ying C, Nan-Nan Z, Hai L, Hua-Sen Z (2013) Understanding of Grounded-Wire TEM Sounding with Near-Source Configuration. J Geophys Remote Sensing 2:113. doi: 10.4172/2169 0049.1000113
Kaufman, A.A., and Keller, G.V., 1983, Frequency and transient sounding: Methods in geochemistry and
geophysics: Elsevier Publ. Co, 1–32.
Nabighian, M.N., and Macnae, J.C., 1991, Time-domain electromagnetic prospecting methods: in Nabighian,
M.N. (ed.), Electromagnetic methods in applied geophysics–Theory volume II, Part A, Society of Exploratio Geophysicists, Tulsa,
Strack K M.Exploration with deep transient electromagnetic method[M], Elsevier,1992
Xue, G.Q., Bai, C.Y., and Yan, Y., 2012, Deep sounding TEM investigation method based on a modified fixed central-loop system: Journal of Applied Geophysics, 76(2012) 23–32.
Xue, G.Q., Wang, H.Y., Yan S., Zhou N.N. 2014, Time-domain Green function solution for transient
electromagnetic field. Chinese Journal geophysics,57(2:671-678)
Zhou Nan-nan, Xue Guo-qiang, Wang He-yuan. Comparison of the time-domain electromagnetic
field from an infinitesimal point charge and dipole source. Applied Geophysics, 2013,10(3):349-356
Ziolkowski A, Hobbs B. A, Wright D (2007) Multi-transient electromagnetic demonstration survey in France.
Geophysics 72: 197-209.

## Slide 23
OMICS International Open Access
Membership enables academic and research institutions, funders and corporations to actively encourage open access in scholarly communication and the dissemination of research published by their authors.
For more details and benefits, click on the link below: http://omicsonline.org/member ship.php